## Slide 1
PATENT UPDATE — M26-026P-PR1-c
Intelligent, Plug-and-Play
Atmospheric Water Harvesting
Code Architecture & Calculation Methodology for Cooling Tower Integration
Prepared by: Mounusha Ram Metti · mmetti@asu.edu Lab: School of Sustainable Engineering and the Built Environment (SSEBE) Date: July 2026

## Slide 2
⚙
CODE · 1 OF 2
Autonomous, Threshold-Triggered Pump Control
pump_controller.py — simplified excerpt
class PumpController:
def auto_check(self, weight_g):
# runs on every new balance reading
w = float(weight_g)
if w > self.threshold_g and not self.is_on:
self.start_timed(self.duration_min)
def start_timed(self, duration_min):
self._turn_on()
if self._timer_thread and self._timer_thread.is_alive():
self._stop_event.set() # cancel prior cycle
self._stop_event = threading.Event()
t = threading.Thread(
target=self._timed_worker,
args=(duration_min, self._stop_event),
)
self._timer_thread = t
t.start()
def _timed_worker(self, duration_min, stop):
waited, step = 0.0, 0.25
limit = duration_min * 60
while waited < limit and not stop.is_set():
time.sleep(step)
waited += step
if not stop.is_set():
self._turn_off()
Why this is “intelligent”
Fully autonomous trigger auto_check() runs on every new balance reading; once a weight threshold is set, no operator input decides when to harvest — the controller decides.
Self-terminating cycle start_timed() launches a background watchdog thread that turns the pump off after duration_min elapses, with no external polling required.
Race-safe restart A trigger arriving mid-cycle cleanly cancels the prior timer (_stop_event) before starting a new one — prevents overlapping or duplicate activations.
Hardware-agnostic bring-up On init, the controller force-frees its GPIO pin via lgpio and runs unmodified on Raspberry Pi 4 or 5 — the same code deploys to a new station with zero configuration changes.
AzAWH — SSEBE, Arizona State University
2

## Slide 3
◎
CODE · 2 OF 2
Sensor Auto-Detection — Hardware-Agnostic by Design
read_balance.py — simplified excerpt
BY_ID_DIR = "/dev/serial/by-id"
MATCH_SUBSTRINGS = ("usb-Prolific_Technology_Inc.",
"USB-Serial_Controller")
def _find_balance_port(self):
# stable by-id symlink; no hardcoded ttyUSB#
if not os.path.isdir(self.BY_ID_DIR):
return None
candidates = []
for name in sorted(os.listdir(self.BY_ID_DIR)):
full = os.path.join(self.BY_ID_DIR, name)
if os.path.islink(full) and all(
s in name for s in self.MATCH_SUBSTRINGS):
candidates.append(full)
if not candidates:
return None
dtech = [c for c in candidates if "Dtech" in c]
return (sorted(dtech) or candidates)[0]
def _resolve_port(self):
# explicit user port always wins over auto-detect
if self.port:
return self.port if os.path.exists(self.port) else None
auto = self._find_balance_port()
return auto if auto and os.path.exists(auto) else None
Why this is “plug-and-play”
No fixed port numbers Linux reassigns /dev/ttyUSB# unpredictably on every reboot or replug; the reader resolves a stable /dev/serial/by-id symlink instead, so wiring order never matters.
Adapter-model tolerant Matching is done on USB descriptor substrings, not an exact device string — different adapter batches or models are recognized automatically.
Deterministic when ambiguous If more than one matching adapter is present, a documented tie-break rule picks one consistently rather than failing or choosing at random.
Repeated per sensor The same pattern (by-id for balance/power meter, by-path for anemometers) is applied independently to every sensor — each self-configures the moment it's plugged in.
AzAWH — SSEBE, Arizona State University
3

## Slide 4
η
CALCULATIONS
Harvesting-Efficiency Physics — Moisture to Capture
es(T) = 6.112 · exp( 17.67·T / (T + 243.5) )
Saturation vapor pressure — Magnus formula, T in °C
AH = 216.7 · (RH/100) · es(T) / (273.15+T) [g/m3]
Absolute humidity — moisture density in the intake air stream
Wintake,i = AHi · vi · A · Δti
Water mass entering the duct; A = 0.18 m², v normalized to m/s from any native unit
ΔWi = max( Wi − Wi-1 , 0 )
Captured water per interval — positive weight gain only, never negative
ηi = min( ΔWi / Wintake,i × 100 , 100 ) %
Per-reading efficiency — capped at 100%; invalid/missing inputs yield 0
ηh = min( ΣΔWi / ΣWintake,i × 100 , 100 ) % (i ∈ hour h)
Hourly efficiency — ratio of hourly totals, not an average of per-reading ratios
Why this is physically grounded
Physically grounded, unit-agnostic Every efficiency figure traces to a real physics quantity — actual moisture mass, not a proxy. Velocity is normalized to m/s from any native anemometer unit before the physics runs, so the same calculation works across sensor models.
Duct geometry & interval accounting A = 0.18 m² converts a velocity reading into volumetric airflow; Δtᵢ is capped at 120 s so a telemetry gap can’t be mistaken for a long airflow interval.
Hourly ≠ average of per-reading ηₕ sums captured and available water across the full hour before dividing — one ratio of totals, not an average of 120 noisy per-minute ratios.
Live in production This exact calculation runs today in the FastAPI backend’s /stations/{id}/hourly endpoint, on real station data.
AzAWH — SSEBE, Arizona State University
4

## Slide 5
✓
VALIDATION
Physical Validation — Cooling Tower Deployment Dataset
11,399
timestamped sensor readings
0.177 m²
measured duct cross-section
(matches the A = 0.18 m² constant used in the code)
~24 hrs
continuous cooling-tower
operating cycle logged
What the dataset contains
A synchronized sensor log from a real cooling-tower AWH installation — balance weight and pump status, voltage/current/power/energy, and intake + outtake air temperature, humidity, and velocity — with the exact Harvesting Efficiency, Absolute Humidity, and kW·h/L columns that are the direct precursor to the equations now running live in the production FastAPI backend. This is the physical dataset the calculation methodology was originally validated against, on a real cooling-tower duct.
AzAWH — SSEBE, Arizona State University
5

## Slide 6
▤
DASHBOARD
Real-Time Visualization — Closing the Loop for the Operator
stations/[id]/page.tsx — simplified excerpt (Next.js / React)
useEffect(() => {
async function fetchHourlyEfficiency() {
const resp = await apiClient.getHourlyAggregation(
stationName,
{ start_date: startDate.toISOString(),
end_date: endDate.toISOString() }
);
// keep only hours with a valid computed value
const points = (resp.data || [])
.filter(r => typeof r.harvesting_efficiency_pct_hourly
=== 'number')
.map(r => ({
date: r.hour,
value: r.harvesting_efficiency_pct_hourly ?? 0,
}));
setHourlyEfficiencyData(points);
}
fetchHourlyEfficiency();
}, [stationName, startDate, endDate]);
Why this matters for the invention
Same formula, live The chart renders ηₕ exactly as computed by the backend’s /stations/{id}/hourly endpoint — no separate client-side reimplementation that could drift out of sync.
Per-station, any date range The operator selects a station and date window; this hook re-fetches and the chart re-renders automatically as those change.
In active use Built on Next.js 15 / React 19 and deployed in production — SSEBE lab staff use it today for day-to-day monitoring across all 8 stations.
Closes the loop Sensing → autonomous control → physics-based calculation → operator-facing visualization, with no manual data-handling step in between.
AzAWH — SSEBE, Arizona State University
6